## Slide 1: Precision Frequency Measurement, Transceiver Calibration, And The frequency measuring Test
George, K1IG
K1IG@arrl.net

## Slide 2
Be sure you’re on the right frequency - avoid an FCC QSL
DX spots are accurate
Does your net complain that you're off frequency?
Digital modes (PSK, WSPR…) require frequency accuracy
Drift with age
Know your rig and be able to optimize its performance
Participate in semi-annual ARRL Frequency Measuring Test
Why Bother?
But my rig has a digital readout! It must be accurate!
X
X
X

## Slide 3: ARRL Frequency Measuring Test
Began in 1931
Twice a year — April and November
Measure frequencies over the air
Goal is 1 Hz or better accuracy — measure and report to the nearest 0.01 Hz
100 - 130 participants worldwide

## Slide 4: Minimum Setup?

## Slide 5: What you need
Rig
These Three Things and Some Free Software
Get You Measuring Within 1 Hz
Computer
Windows
Mac
Linux
Audio Cable

## Slide 6: Three Step Process
Load software and set it up
Calibrate your computer
Calibrate your rig
Total Time = One Hour

## Slide 7: Free Software
Spectrum Lab
  http://www.qsl.net/dl4yhf/spectra1.html
Installation tutorial at:
  http://www.ve2azx.net/technical/FMT/SpecLabInfo.pdf
Windows
Mac/Linux/Windows
Fldigi
  http://www.w1hkj.com/Fldigi.html
  Download, installation and help files on main webpage
WSPR
  http://physics.princeton.edu/pulsar/K1JT/wspr.html
  http://physics.princeton.edu/pulsar/K1JT/FMT_User.pdf

## Slide 8: Spectrum Lab
Very versatile and accurate
Will run in Linux/Wine or Mac/Parallels at reduced capability

## Slide 9: Spectrum Lab setup
Select sound card
Set Sample Rate to 44100
Hit Apply

## Slide 10: Spectrum Lab setup
Try these settings. If the display freezes, reduce them. Accuracy will suffer.

## Slide 11: W W V

## Slide 12: Computer Calibration
2-3 hour warm-up
Tune to any W W V in AM mode
Measure frequency during 600 Hz tone
Apply correction
Avoid sunrise/sunset times (WWV Doppler)
1
2
3
4

## Slide 13: Computer Calibration
After calibration, we’re within 0.0023 Hz

## Slide 14: Rig Calibration
Set rig to USB
Tune to 15 MHz W W V
Re-tune to 14,999.400 KHz = W W V - 600 Hz
Measure the frequency of the carrier
Adjust your rig (if possible) to center the carrier at 600 Hz — consult manual

## Slide 15: Rig Calibration
Measure all W W V and CHU frequencies (-600 Hz)
Make a correction chart based on WWV and CHU measurements

## Slide 16: fldigi
Ref: FLDIGI Users Manual - Operating
  Digiscope Display - W W V mode
  Frequency Analyzer (v. 3.21)
Ref: FLDIGI Users Manual - Operating
  Digiscope Display - W W V mode
  Frequency Analyzer (v. 3.21)

## Slide 17: fldigi setup
Computer Calibration — Part I
  Select Op Mode - W W V
  Select View - Floating Scope
  Select Configure - Sound Card
Make corrections here

## Slide 18: fldigi setup
Computer Calibration — Part II
  Set Rig to AM — tune to any W W V
  Apply “RX ppm” corrections to make the scope line vertical
    Ref: FLDIGI Users Manual
      Digiscope Display — W W V Mode
-1000 ppm
+1000 ppm

## Slide 19: fldigi rig calibration
You’ll get a data file that you can import into a spreadsheet
Set Rig to USB — tune to W W V - 600 Hz
Select Op Mode - Freq Analysis
Adjust rig so waterfall is exactly at 600 Hz
writing csv file

## Slide 20: Frequency Measuring
Tune below frequency so sidetone is about 600 Hz
Tuner + Spectrum Lab ± Offset = Frequency
9,979,400 + 590.252 - 0.141 = 9,979,990.111 Hz
Offset error = +0.141 Hz

## Slide 21: Frequency measuring test
Test Format (three frequencies):
5 minute call-up
2 minute test (carrier or tone)
1 minute sign-off
Go to designated website and enter data to nearest .01 Hz
  Perform calibrations before and after the test!
Test announcement in QST and:
        http://www.arrl.org/frequency-measuring-test
Data entry page and previous results are at:
        http://www.b4h.net/fmt/
Actuals to nearest 0.01 Hz

## Slide 22: techniques for the truly serious
fanatical*
Record the test as a WAV file and play it back on other computers for analysis
Feed a 10 MHz GPSDO (GPS Disciplined Oscillator) signal into your receiver and computer for nanosecond accuracy
Warm up receiver for 48 hours in a temperature controlled blanket
* No guarantee of accuracy improvement

## Slide 23: Rig calibration
EXACT!